## Slide 1: Modelling the Morphodynamic Response To Flow Regulation In An Artificial Reservoir
Luca Cortese1, Mark Behn1, Anthony Edgington1, Sydney Crisanti2, Travis Dahl2, Christopher Sheehan3, Danielle Tarpley2, Amanda Tritinger2, and Noah Snyder1
1Boston College, Earth and Environmental Sciences, Chestnut Hill, MA, United States of America
2Coastal and Hydraulics Laboratory, U.S. Army Engineer Research and Development Center, Vicksburg, MS, United States of America
3College of Arts and Sciences: Earth and Environmental Geosciences, University of Dayton, Dayton, OH, United States of America
Contact: cortel@bc.edu
Session: HS9.2 – EGU26-13816
Vienna 7 May 2026

## Slide 2: Why do we care about sediment in reservoirs?
Greg Morris, GLM Engineering
Drawbacks of sedimentation (just a few)
Storage reduction
Interference with dam operations
Reduced hydropower reliability
Dam safety risks and machinery damage
Downstream erosion
Randle et al. (2019)
Singh Thapa et al. (2015)

## Slide 3: Goal: estimate sedimentation across Lake Seminole
Chattahoochee arm | Flint arm
Level of management | 
High | Low
Sub-daily hydropeaking | Natural (seasonal) flow
Depositional characteristics | 
Subaerial delta | Subaqueous only
Reservoir operations
Constant water level
Annual water volume inflow
Similar between the two rivers

## Slide 4: A Delft3D-FM model to estimate sedimentation
Hydrodynamics
Sediment transport
Bed evolution
Control water level
2D depth-averaged model
Delft3D-FM
(Flexible Mesh)
RTC
(Real Time Control)
Calibration/Validation | 
Hydrodynamic model | Flow velocity from ADCP
Sediment transport | SSC samples
Bed evolution | Sedimentation rates from cores

## Slide 5: Chattahoochee and Flint waters have limited mixing
Mixing only in proximity of the dam
Particle tracking dorado (Hariharan et al., (2020)
Hariharan et al., (2020). dorado: A Python package for simulating passive particle transport in shallow-water flows. Journal of Open Source Software, 5(54), 2585, https://doi.org/10.21105/joss.02585

## Slide 6: Hydropeaking regulates sediment delivery in the Chattahoochee
Cohesive fraction
Suspended sediment transport is silt-dominated

## Slide 7: Sedimentation is highly heterogeneous
The model reproduces the measured sedimentation rates
Two very distinct depositional patterns
On average, the lake accumulates sediment at about 1 cm/yr (Trapping efficiency of 78%)

## Slide 8: In summary …
Thank you! Any questions? Contact: cortel@bc.edu
The 2 arms are disconnected until proximity of the dam
Hydropeaking mobilizes higher volumes of sediments in the Chattahoochee
Different types of deposition: sedimentation is NOT an issue in Lake Seminole (for now…)